## Slide 1
School of Mechanical and Control Engineering Prof. YoungKeun-Kim
22000355 HyeonGyu-Seo 22200757 Joungbin Choi
한동대학교
25-1 DLIP Final Project Proposal
Vibration Frequency Estimation via
AI-Based Motion Magnification

## Slide 2: Introduction
Machine Defects
Problem Statement
Condition monitoring of existing industrial facilities is performed based on physical sensors.
This project aims to implement non-contact sensing technology
Using Motion Magnification to amplify micro-vibrations in images
Situations where physical sensor attachment is difficult - high temperature/high pressure environment, narrow space, moving objects, etc.
Sensor environment vulnerable to noise - magnetic field interference, structural vibration confusion
When single component vibration localization is required - status analysis of specific parts, not the entire facility

## Slide 3: Goal of Project & Target Customers
The Main Goal
To solve the problems mentioned in the problem statement, we want to analyze vibrations using cameras and deep learning models. This will allow us to predict the possibility of failure and prevent plant losses.
Target Performance
Model
  PSNR > 25.0 dB
  SSIM > 0.9
Visualization & Detect Vibration
  XT-Slice Visualization
  Image Processing
Target Customers
Smart Factory Integrators – for condition monitoring of machines in automated manufacturing environments
Plant Maintenance Service Providers – where large-scale equipment needs frequent non-invasive inspection
Robot Health Diagnostics Companies – enabling remote or visual-based state estimation for robots or mechatronic systems

## Slide 4
Magnification Model Architecture
Encoder
  Decompose input frame into two components
  Shape Representation (M)
  Texture Representation (V)
Manipulator
  non-linear processing via convolution
Decoder
  Combines the manipulated shape and texture.
  Reconstructs the magnified output frame.

## Slide 5
Create Train Dataset
Extract frames from video
Construct input pairs (Xa, Xb)
Estimate pixel movement between two consecutive frames
Generate target (Y) using Optical Flow warping
Input video.mp4
Xa()
Xa()
dx(Horizontal)
dy(Vertical)
Warped Y (x 10.0)
여기다 실험 세팅 한거 사진 하나?

## Slide 6
Evaluation
PSNR (Peak Signal-to-Noise Ratio)
  The loss information on the image quality
  The higher the value, the less the loss.
SSIM (Structural Similarity Index Map)
  Evaluates quality in three aspects: Luminance, Contrast, and Structural.

## Slide 7
Evaluation
Ground Truth
Ours (SF=10)
This image
Set 10 means
29.42/0.9528
25.05/0.9362
Ours (SF=30)
29.32/0.9516
24.66/0.9329
Ours (SF=50)
28.75/0.9470
24.22/0.9252
Deepmag (SF=50)
28.51/0.9427
23.98/0.9129
Deepmag (SF=30)
29.02/0.9477
24.61/0.9256
Deepmag (SF=10)
29.38/0.9510
24.66/0.9318
Ground Truth
This image
Set 10 means

## Slide 8
Evaluation

## Slide 9
Image processing
Create X-T (Horizontal)
Periodicity of Slice Image → Image-based Vibration Frequency Estimation Possible
  Display analysis coordinates as lines for each frame
  Find contours in the edge image and consider each as a "vibration waveform".
X-T slice Video
Magnified Video
Magnified Video

## Slide 10
Result